## Slide 1: Auto Cum Manual Fire Combat Aid
--Team:The Initiators🚀
~S.K.Hari Kheshav
~M Ashwin Kumar

## Slide 2: Objective:
This project is a Fire combat Aid which can be controlled both automatically in a emergency case and manually after the beholder gains control to the situation.
It also does not have an external remote which needs to be searched during an emergency rather it could be connected to a smartphone app which works as the remote.
Also during too unfortunate situations in which the robot itself is in danger or the fire goes uncontrollable the robot gives a sign to the nearest fire station using the preexisting phone number using the smartphone.

## Slide 3: Circuit Diagram

## Slide 4: Apparatus:
Arduino Uno is a microcontroller board based on the ATmega328P . It has 14 digital input/output pins (of which 6 can be used as PWM outputs), 6 analog inputs, a 16 MHz quartz crystal, a USB connection, a power jack, an ICSP header and a reset button. It contains everything needed to support the microcontroller; simply connect it to a computer with a USB cable or power it with a AC-to-DC adapter or battery to get started.. You can tinker with your UNO without worring too much about doing something wrong, worst case scenario you can replace the chip for a few dollars and start over again.

## Slide 5: Apparatus:
HC-05 module is an easy to use Bluetooth SPP (Serial Port Protocol) module, designed for transparent wireless serial connection setup. Serial port Bluetooth module is fully qualified Bluetooth V2.0+EDR (Enhanced Data Rate) 3Mbps Modulation with complete 2.4GHz radio transceiver and baseband.

## Slide 6: Apparatus:
A flame sensor module that consists of a flame sensor (IR receiver), resistor, capacitor, potentiometer, and comparator LM393 in an integrated circuit. It can detect infrared light with a wavelength ranging from 700nm to 1000nm.The far-infrared flame probe converts the light detected in the form of infrared light into current changes. Sensitivity is adjusted through the onboard variable resistor with a detection angle of 60 degrees.
Working voltage is between 3.3v and 5.2v DC, with a digital output to indicate the presence of a signal. Sensing is conditioned by an LM393 comparator

## Slide 7: Apparatus:
Servo motors control position and speed very precisely. Now a potentiometer can sense the mechanical position of the shaft. Hence it couples with the motor shaft through gears. The current position of the shaft is converted into electrical signal by potentiometer, and is compared with the command input signal. In modern servo motors, electronic encoders or sensors sense the position of the shaft .
We give command input according to the position of shaft . If the feedback signal differs from the given input, an error signal alerts the user. We amplify this error signal and apply as the input to the motor, hence the motor rotates. And when the shaft reaches to the require position , error signal become zero , and hence the motor stays standstill holding the position.

## Slide 8: Apparatus:
L293D Motor Driver is a module for motors that allows you to control the working speed and direction of two motors simultaneously .This Motor Driver is designed and developed based on L293D IC.
L293D is a 16 Pin Motor Driver IC. This is designed to provide bidirectional drive currents at voltages from 5 V to 36 V as Arduino won’t be able to provide maximum current.
DC motor (BO) Battery Operation. Dc motor converts electrical energy into mechanical energy. Why DC gear motor used in robot Motor control circuit. DC MOTOR concept is where gears reduce the speed of the vehicle but increase its torque is known as gear reduction. In DC motor is assembled with multiple gear setup.

## Slide 9: Apparatus:
Pump Motor:

## Slide 10: Program
The programming of the robot is divided into two parts:
Arduino IDE:An Arduino IDE is used to control the circuit part of the robot. It has an HC05 Bluetooth Controller which thereby sends and receives necessary commands to the app.
MIT APP Inventor:It is not a perfect example for programming as it doesn’t require coding.Rather it stimulates necessary conditions by by pressing the button. Though it is used to control the robot by sending necessary commands which inturn activates specific functions in an Arduino.

## Slide 11: Economics:
A normal fire fighting robot costs about $3500 in Alibaba.com rather our robot’s making cost is lesser than RS.3500.i.e., about 70 times lesser. Even though the worker cost might increase the total making the process is easy to automate and would get more cheaper if we start using Printed Circuit Boards, Bootloaded Microcontrollers thereby reducing wire costs.

## Slide 12: Applications:
Could be used to access areas inaccessible by firefighters.
Cost effective and thereby could be bought by individual homes and commercial purposes.
Easy to upgrade as it uses Arduino and App Inventor which engages freelancers who are interested.
Easy to control and child friendly.

## Slide 13: Bibliography:
Wikepedia
CircuitDigest
Arduino.cc
MitAppInventor
Amazon
Arduino Sensors App
Arduino Programming

## Slide 14: Guidances:
Mr.Keshav: Student
Mr.Loganathan:Faculty
Mr.Sandeep:Ex Student
Many other friends,and references.